## Slide 1
1
IoT PROJECT PITCH
Indoor Asset
Localization System
Using LoRa + ESP32 + ThingsBoard
Sandy George · Marina Medhat · Youssef Khalil · Rubina Sameh
April 30, 2026

## Slide 2
TABLE OF CONTENTS
Contents
01
Introduction & Problem Statement
02
Related Work & Existing Limitations
03
Proposed Solution
04
System Architecture
05
Implementation Plan & Timeline
06
Progress So Far
07
Challenges & Next Steps
p. 3
p. 4
p. 5
p. 6
p. 7
p. 8
p. 9
2

## Slide 3
3
01 · INTRODUCTION
Introduction & Problem Statement
The Problem
In universities, hospitals, offices and labs, important assets are frequently misplaced or take too long to locate.
This causes:
Wasted time searching for devices & tools
Lower operational efficiency
Interruptions in daily workflows
No automated visibility of asset locations
Why It Matters
Who is affected?
Lab supervisors, nurses, office employees,
technicians & facility managers
Current gap:
No IoT-native indoor tracking solution
that is low-power, low-cost, and works
without GPS or complex infrastructure.
Notes: "Staff spend real time hunting for equipment. There's no automated system that says where something is inside a building."

## Slide 4
3
02 · RELATED WORK
Related Work & Existing Limitations
GPS Tracking
Does not work indoors, no satellite signal penetration
Bluetooth BLE Beacons
Short range (~10 m), requires dense infrastructure, high power
Wi-Fi Fingerprinting
Requires site surveys, high computation, infrastructure-heavy
RFID Systems
Read range limited to centimetres–metres; needs specialized readers at every door
UWB (Ultra-Wideband)
Very accurate but expensive hardware and complex anchor setup
Our Gap: A low-power, LoRa-based indoor localization system with cloud dashboard , therefore, practical for real buildings at low cost.
Notes: "GPS fails indoors. BLE needs dense infrastructure. RFID is centimetre-range. Our LoRa approach hits the sweet spot: long indoor range, low power, low cost."

## Slide 5
4
03 · PROPOSED SOLUTION
Proposed Solution
Indoor Asset Localization System Using LoRa — track assets via RSSI-based zone estimation, forwarded to ThingsBoard cloud dashboard
📡 LoRa Tags on Assets
Each tracked asset carries a LoRa transmitter broadcasting a unique asset ID every 3 seconds
📥 ESP32 Receiver Node
Fixed receiver captures packets, measures RSSI & SNR, classifies into proximity zone
☁️ Wi-Fi → ThingsBoard
ESP32 forwards readings via HTTP POST to ThingsBoard cloud for storage & visualization
🗺️ Live Dashboard
Real-time zone display (NEAR / MID / FAR / OUT OF RANGE) with asset ID, RSSI & timestamp
Notes: "The asset carries a tag. A fixed node hears it. The cloud stores it. The dashboard shows where it is — all automatically."

## Slide 6
5
04 · SYSTEM ARCHITECTURE
System Architecture
LoRa
Transmitter
(Asset Tag)
►
ESP32
LoRa Receiver
+ OLED
►
Wi-Fi
Network
►
ThingsBoard
Cloud
►
Dashboard
(Browser)
LoRa 868 MHz
LoRa → Wi-Fi
HTTP POST
API / WS
Hardware Components
Component | Role | Protocol
LoRa Tag / Transmitter | Broadcasts asset ID | LoRa
ESP32 + LoRa Module | Receives signal, measures RSSI, forwards data | LoRa + Wi-Fi
Wi-Fi Router | Connects ESP32 to cloud | Wi-Fi
ThingsBoard Cloud | Stores data, runs zone logic, serves dashboard | HTTP / WS
Component Role Protocol

## Slide 7
6
05 · IMPLEMENTATION PLAN
Implementation Plan
Week 1
Apr 23–29
Assign Tx/Rx roles
Flash Sender & Receiver firmware
Test LoRa link, log RSSI locally
Define test zones & backend skeleton
Week 2
Apr 30–May 6
Wi-Fi forwarding, DB logging & RSSI calibration
Week 3
May 7–13
Zone logic, floor map dashboard & end-to-end test
Week 4
May 14–20
Validation, tuning & final report
✅ Week 1 COMPLETE
Notes: "We're presenting at the end of Week 1 — hardware is up, firmware works, pipeline is started. Three weeks remain for calibration, dashboard, and validation."

## Slide 8
7
06 · PROGRESS SO FAR
Progress So Far — Week 1 Complete
Sender firmware: broadcasts LAPTOP-001|PKT:N every 3 s on 868 MHz, SF7, BW 125 kHz
Receiver firmware: parses packet, reads RSSI & SNR, classifies zone, displays on OLED
Zone classification logic: NEAR (<–60 dBm) / MID (<–80) / FAR (<–100) / OUT OF RANGE
Wi-Fi + NTP time sync implemented (UTC+2 Egypt)
ThingsBoard HTTP POST sending assetID, RSSI, SNR, zone as JSON telemetry
OLED display output confirming live packet reception
Key Code Snippets
// Sender (Project_Sender.ino)
String msg = assetID + "|PKT:" + counter;
// Receiver — Zone logic
if (rssi > -60) return "NEAR";
if (rssi > -80) return "MID";
if (rssi > -100) return "FAR";
// Send to ThingsBoard
http.POST("{assetID, rssi, snr, zone}");

## Slide 9
8
07 · CHALLENGES & NEXT STEPS
Challenges & Next Steps
Current Challenges
Only 2 LoRa Modules
Limits us to coarse RSSI zones — true triangulation needs 3+ nodes
RSSI Variability
Multipath reflections & obstacles cause fluctuation; requires calibration per environment
Single Asset Tracking
Current prototype tracks one asset; multi-asset requires ID-based multiplexing
Wi-Fi Dependency
Receiver needs stable Wi-Fi; dead spots could drop readings to backend
Next Steps (Weeks 2–4)
1
Wi-Fi + DB pipeline
Connect ESP32 to ThingsBoard, verify live storage
2
RSSI Calibration
Measure at 3–5 distances, set realistic thresholds
3
Floor Map Dashboard
Real-time zone map, no manual refresh required
4
Multi-asset simulation
Add simulated asset IDs to test dashboard scalability
5
Power Measurement
Measure current draw on Tx/Rx (mandatory bonus feature)

## Slide 10
9
Thank You
Questions?